## Slide 1
SCHEMA DE CALCUL

## Slide 2
Schéma de calcul et interface de modules exemple très simplifié
initialize : [IM_3, IM_4]
run : [IM_1, IM_2, IM_3, IM_4, IM_5]
end_simulation : [IM_3, IM_6}
IM_1 : WallLosses run
dict(space):
inside_air_temperatures
float(project):
exterior_air_temperature
dict(boundary):
q_walls
IM_2 : Generator run
dict(space):
q_needs
dict(emitter):
q_provided
IM_3 : ThermalSpace
initialize
run
end_simulation
dict(boundary):
q_walls
dict(emitter):
q_provided
dict(space):
Inside_air_temperatures
dict(space):
q_needs
IM_4 : Weather
initialize
run
float(project):
exterior_air_temperature
IM_5 : Occupants
run
dict(space):
setpoint_temperatures
dict(space):
gains
IM_6 : ACV
end_simulation
float:
co2_impact
float(project):
Annual_needs
dict(emitter):
q_consumed
dict(space):
setpoint_temperatures
dict(space):
gains
dict(space):
previous_inside_air_temperatures
dict(emitter): q_consumed
Légende :
dict(objet): variable
Dictionnaire avec la valeur de la variable pour chaque objet du projet

## Slide 3
COLLECTION DE MODULES
ASSOCIES AU SCHEMA
2x IM_1
2x IM_2
1x IM_3
1x IM_4
1x IM_5
1x IM_6

## Slide 4: Collections de modules pour IM_1
Nom : SimplifiedWallLosses
Module_Id : M1a
IM_compatibility : IM_1 (WallLosses)
Input(s) | Format | Object scope
exterior_air_temperature | float | weather. exterior_air_temperature
inside_air_temperatures | dict | project_data.space. inside_air_temperature (float)
Output(s) | Format | Object scope
q_walls | dict | boundary.q_walls (float)
Parameter(s) | Format | Object scope
u_value | float | boundary.u_value
area | float | boundary.area
run
For each boundary in project_data.boundaries:
self.q_walls(boundary.id) = boundary.u_value * boundary.area *
(boundary.space.inside_air_temperature – self.exterior_air_temperature)

## Slide 5: Collections de modules pour IM_1
Nom : LayerWallLosses
Module_Id : M1b
IM_compatibility : IM_1 (WallLosses)
Input(s) | Format | Object scope
exterior_air_temperature | float | weather. exterior_air_temperature
inside_air_temperatures | dict | project_data.space. inside_air_temperature (float)
Output(s) | Format | Object scope
q_walls | dict | boundary.q_walls (float)
Parameter(s) | Format | Object scope
thickness | float | boundary.layer.thickness
thermal_conductivity | float | boundary.layer.thermal_conductivity
area | float | boundary.area
run
For each boundary in project_data.boundaries:
thermal_resistance =
thermal_conductance = 1/thermal_resistance
self.q_walls(boundary.id) = thermal_conductance * boundary.area *
(boundary.space.inside_air_temperature – self.exterior_air_temperature(t))

## Slide 6: Collections de modules pour IM_2
Nom : InfinitePowerGenerator
Module_Id : M2a
IM_compatibility : IM_2 (Generator)
Input(s) | Format | Object scope
q_needs | dict | space.q_needs (float)
Output(s) | Format | Object scope
q_provided | dict | emitter.q_provided (float)
q_consumed | dict | emitter.q_consumed (float)
Parameter(s) | Format | Object scope
efficiency | float | emitter.efficiency
run
For each space in project_data.spaces:
number_of_emitters = nombre d’émetteurs appartenant/rattachés/liés au space via la boundary
for each emitter in space:
self.q_consumed(emitter.id) = self.q_needs(space.id) / (number_of_emitters * emitter.efficiency)
self.q_provided(emitter.id) = self.q_needs(space.id) / number_of_emitters

## Slide 7: Collections de modules pour IM_2
Nom : LimitedGenerator
Module_Id : M2b
IM_compatibility : IM_2 (Generator)
Input(s) | Format | Object scope
q_needs | dict | space.q_needs (float)
Parameter(s) | Format | Object scope
efficiency | float | emitter.efficiency
pn | float | emitter.efficiency
Output(s) | Format | Object scope
q_provided | dict | emitter.q_provided (float)
q_consumed | dict | emitter.q_consumed (float)
run
For each space in project_data.spaces:
max_q = somme des pn des émetteurs appartenant/rattachés/liés au space via la boundary
q_total_provided = min(max_q, self.q_needs(space.id))
for each emitter in space:
self.q_consumed(emitter.id) = q_total_provided / ((max_q/emitter.pn) * emitter.efficiency)
self.q_provided(emitter.id) = q_total_provided / (max_q/emitter.pn)

## Slide 8: Collections de modules pour IM_3
Nom : ThermalSpaceSimplified
Module_Id : M3
IM_compatibility : IM_3 (ThermalSpace)
Input(s) | Format | Object scope
q_walls | dict | boundary.q_walls (float)
setpoint_temperatures | dict | space.setpoint_temperature (float)
q_provided | dict | emitter.q_provided (float)
gains | dict | space.gains (float)
previous_setpoint_temperatures | dict | space.previous_setpoint_temperature (float)
q_needs | dict | space.q_need (float)
inside_air_temperatures | dict | space.inside_air_temperature (float)
q_needs | dict | space.q_needs (float)
annual_needs | dict | space.annual_needs (float)
Parameter(s) | Format | Object scope
reference_area | Float | Space.reference_area
height | float | space.height
run
For each space in project_data.spaces:
q_walls = sum(self.q_walls for each boundary of the space)
Tint_t = self.setpoint_temperatures(space.id)
Tint_tp = self.previous_setpoint_temperatures(space.id)
self.q_needs(space.id) = max(0,(Tint_t – Tint_tp) * (thermal_capacity * space.reference_area * space.height) + q_walls – self.gains(space.id))
self.temporary_annual_needs(space.id) += [(Tint_t - self.previous_setpoint_temperature)*(thermal_capacity * space.surface * space.height) + q_walls – self.gains(space.id)] / space.surface
q_effective = q_provided(space.emitter.id) + self.gains(space.id) – q_walls
self.setpoint_temperatures(space.id)= Tint_tp + q_effective / (thermal_capacity * space.surface * space.height)
initialize
For each space in project_data.spaces:
self.inside_air_temperatures(space.id) = 20°C
self.previous_setpoint_temperature = 20°C
self.temporary_annual_needs(space.id) = 0
constante de model
thermal_capacity : 0,335Wh/m3.K
end_simulation
For each space in project_data.spaces:
self.annual_needs(space.id) = self.temporary_annual_needs(space.id)

## Slide 9: Collections de modules pour IM_4
Nom : WeatherModel
Module_Id : M4
IM_compatibility : IM_4 (Weather)
Input(s) | Format | Object scope
Output(s) | Format | Object scope
exterior_air_temperature | float | project
Parameter(s) | Format | Object scope
altitudes | list(float) | building.altitudes
scenario_exterior_air_temperatures | list(float) | weather
constante de model
temperature_diminution_with_altitude = 0,0065 °C/m
run
self.exterior_air_temperature = self.corrected_exterior_air_temperatures
initialize
mean_altitude = moyenne(self.altitudes)
For each i, temperature in scenario_exterior_air_temperatures:
# Hypothese le fichier météo est a 0m d’altitude
self.corrected_exterior_air_temperatures(i) = temperature – self.temperature_diminution_with_altitude * mean_altitude

## Slide 10: Collections de modules pour IM_5
Nom : OccupantModel
Module_Id : M5
IM_compatibility : IM_5 (Occupants)
Input(s) | Format | Object scope
Output(s) | Format | Object scope
setpoint_temperatures | dict | space.setpoint_temperature (float)
gains | dict | space.gains (float)
Parameter(s) | Format | Object scope
reference_area | float | space.reference_area
presence_setpoint_temperature | dict | space.presence_setpoint_temperature
absence_setpoint_temperature | dict | space.absence_setpoint_temperature
occupation (list int 8760) | dict | space.occupation
run
For each space in project_data.spaces:
self.gains(space.id) = self.occupation * self.occupant_per_square_meter * space.surface * self.occupant_gains
if space.occupation(t) > 0:
self.setpoint_temperatures(space.id) = space.presence_setpoint_temperature
else:
self.setpoint_temperatures(space.id) = space.absence_setpoint_temperature
constante de model
occupant_per_square_meter : 1/40
occupant_gains : 100W

## Slide 11: Collections de modules pour IM_6
Nom : ACVExploitationOnlyModel
Module_Id : M6
IM_compatibility : IM_6 (ACV)
Input(s) | Format | Object scope
q_consumed | dict | emitter.q_consumed (float)
Output(s) | Format | Object scope
Co2_impact | float | project
Parameter(s) | Format | Object scope
end_simulation
self.co2_impact = self.carbon_to_electricity_ratio * sum(self.q_consumed)
constante de model
carbon_to_electricity_ratio: 70 gCO2/kWh

## Slide 12
BACKBONE
CHOIX DE MODE DE RESOLUTION
CHOIX DES MODULES

## Slide 13: Choix des modules
Les variables de simulations des project objects ne changent pas selon le choix des modules par définition des IM. En revanche les paramètres oui.
Space
Inside_air_temperature
q_needs
setpoint_temperature
gains
annual_needs
surface
height
absence_setpoint_temperature
presence_setpoint_temperature
occupation
Boundary
q_wall
u_value
area
Weather
exterior_air_temperature
scenario_exterior_air_temperatures
Emitter
q_provided
efficiency
Project
co2_impact
altitudes
Ex : Si choix suivants : IM_1 = M1a | IM_2 = M2a | IM_3 = M3 | IM_4 = M4 | IM_5 = M5 | IM_6 = M6

## Slide 14: Choix des modules
Les variables de simulations des project objects ne changent pas selon le choix des modules par définition des IM. En revanche les paramètres oui.
Space
Inside_air_temperature
q_needs
setpoint_temperature
gains
annual_needs
surface
height
absence_setpoint_temperature
presence_setpoint_temperature
occupation
Boundary
q_wall
thickness
conductivity
Weather
exterior_air_temperature
scenario_exterior_air_temperatures
Emitter
q_provided
efficiency
pn
Project
co2_impact
altitudes
Ex : Si choix suivants : IM_1 = M1b | IM_2 = M2b | IM_3 = M3 | IM_4 = M4 | IM_5 = M5 | IM_6 = M6

## Slide 15
CAS APPLICATION & MODELE DE DONNEE ASSOCIE
AU SCHEMA EXEMPLE
2 exemples présentés mais 4 combinaisons possible de choix de modules interchangeable

## Slide 16
Ex 1 : Si choix suivants : IM_1 = M1a | IM_2 = M2a | IM_3 = M3 | IM_4 = M4 | IM_5 = M5 | IM_6 = M6
Exemple sur 12h (12 pas de temps)
Building (id = 1)
altitude = 250
Space1 (id = 1)
reference_area = 50
height = 2.5
presence_setpoint_temperature = 20
absence_setpoint_temperature = 17
occupation = [1,1,1,1,1,0,0,0,1,1,1,1]
Space2 (id = 2)
reference_area = 30
height = 2.5
presence_setpoint_temperature = 20
absence_setpoint_temperature = 17
occupation = [1,1,1,1,1,0,0,0,0,0,0,0]
Weather (id = 1)
scenario_exterior_air_temperatures = [9,12,13,14,18,21,21,16,12,11,9,9]
Boundary1 (id = 11)
u_value = 1
area = 25
Boundary2 (id = 12)
u_value = 0,3
area = 13
Boundary3 (id = 13)
u_value = 0,35
area = 15
Emitter1 (id = 21)
efficiency = 0.85
Emitter2 (id = 22)
efficiency = 0.60
Emitter3 (id = 23)
efficiency = 0.90

## Slide 17
Ex 1 : Si choix suivants : IM_1 = M1b | IM_2 = M2b | IM_3 = M3 | IM_4 = M4 | IM_5 = M5 | IM_6 = M6
Exemple sur 12h (12 pas de temps)
Building (id = 1)
altitude = 250
Space1 (id = 1)
reference_area = 50
height = 2.5
presence_setpoint_temperature = 20
absence_setpoint_temperature = 17
occupation = [1,1,1,1,1,0,0,0,1,1,1,1]
Space2 (id = 2)
reference_area = 30
height = 2.5
presence_setpoint_temperature = 20
absence_setpoint_temperature = 17
occupation = [1,1,1,1,1,0,0,0,0,0,0,0]
Weather (id = 1)
scenario_exterior_air_temperatures = [9,12,13,14,18,21,21,16,12,11,9,9]
Boundary1 (id = 11)
thermal_conductivity = [0.25, 0.035, 1.5]
Thickness = [0.02, 0,0275, 0.2]
area = 25
Boundary2 (id = 12)
lambda=[0.25, 0.035, 1.5] thickness=[0.02, 0,1092, 0.2]
area = 13
Boundary3 (id = 13)
thermal_conductivity = [0.25, 0.035, 1.5] thickness = [0.02, 0,0925, 0.2]
area = 15
Emitter1 (id = 21)
efficiency = 0.85
pn = 100W
Emitter2 (id = 22)
efficiency = 0.60
pn = 80W
Emitter3 (id = 23)
efficiency = 0.90
pn = 100W